## Slide 1: INTERNATIONAL INSTITUTE OF PROFFESIONAL STUDIES -DAVV
DIGITAL COMPUTER ORGANIZATION
AADYA MATHUR
MCA-SEM 3rd(sec A)

## Slide 2
1. Introduction to Computer Organization

## Slide 3: Introduction to Computer Organization
It is the way the hardware components operate.
Organization is how features are implemented
Control signals, interfaces, memory technology.

## Slide 4
Computer organization and architecture mainly focuses on various parts of the computer in order to reduce the execution time of the program, improve the performance of each part. Generally, we tend to think computer organization and computer architecture as same but there is slight difference.
Computer Organization is study of the system from software point of view and gives overall description of the system and working principles without going into much detail. In other words, it is mainly about the programmer’s or user point of view.
Computer Architecture is study of the system from hardware point of view and emphasis on how the system is implemented. Basically, throws light on the designer’s point of view.

## Slide 5: Von Neumann Architecture
The modern computers are based on a stored-program concept introduced by John Von Neumann.
In this stored-program concept, programs and data are stored in a separate storage unit called memories and are treated the same.
It is having three basic units:
1.The Central Processing Unit (CPU)
2.The Main Memory Unit
3.The Input/output Device

## Slide 6: Von Neumann Architecture
Control Unit : A control unit (CU) handles all processor control signals.
It directs all input and output flow.
Fetches code for instructions and controlling how data moves around the system.
Arithmetic and Logic Unit (ALU):
The arithmetic logic unit is that part of the CPU that handles all the calculations the CPU may need.
e.g. Addition, Subtraction, Comparisons. It performs Logical Operations, Bit Shifting Operations, and Arithmetic Operation

## Slide 7: Von Neumann Architecture
Main Memory Unit (Registers)
Accumulator: Stores the results of calculations made by ALU.
Program Counter (PC): Keeps track of the memory location of the next instructions to be dealt with. The PC then passes this next address to Memory Address Register (MAR).
Memory Address Register (MAR): It stores the memory locations of instructions that need to be fetched from memory or stored into memory.
Memory Data Register (MDR): It stores instructions fetched from memory or any data that is to be transferred to, and stored in, memory.

## Slide 8: Von Neumann Architecture
Current Instruction Register (CIR): It stores the most recently fetched instructions while it is waiting to be coded and executed.
Instruction Buffer Register (IBR): The instruction that is not to be executed immediately is placed in the instruction buffer register IBR
Input/output Devices :
Program or data is read into main memory from the input device or secondary storage under the control of CPU input instruction. Output devices are used for display.

## Slide 9: Vonn Neumann Architecture

## Slide 10: Bus Connections
Data is transmitted from one part of a computer to another, connecting all major internal components to the CPU and memory, by the means of Buses. Basically buses are of three types:
Data Bus: It carries data among the memory unit, the I/O devices, and the processor.
Address Bus: It carries the address of data (not the actual data) between memory and processor.
Control Bus: It carries control commands from the CPU (and status signals from other devices) in order to control and coordinate all the activities within the computer.

## Slide 11: INTERCONNECTION STRUCTURES
A computer consists of a set of components or modules of three basic types (processor, memory, I/O) that communicate with each other. In effect, a computer is a network of basic modules. Thus, there must be paths for connecting the modules. The collection of paths connecting the various modules is called the interconnection structure. The design of this structure will depend on the exchanges that must be made among modules.

## Slide 12
Memory: Typically, a memory module will consist of N words of equal length. Each word is assigned a unique numerical address (0, 1, . . . , N – 1). A word of data can be read from or written into the memory. The nature of the operation is indicated by read and write control signals. The location for the operation is specified by an address.
I/O module: From an internal (to the computer system) point of view, I/O is functionally similar to memory. There are two operations, read and write. Further, an I/O module may control more than one external device. We can refer to each of the interfaces to an external device as a port and give each a unique address (e.g., 0, 1,…, M – 1). In addition, there are external data paths for the input and output of data with an external device. Finally, an I/O module may be able to send interrupt

## Slide 13
Processor: The processor reads in instructions and data, writes out data after processing, and uses control signals to control the overall operation of the system. It also receives interrupt signals. The preceding list defines the data to be exchanged. The interconnection structure must support the following types of transfers:
• Memory to processor: The processor reads an instruction or a unit of data from memory. • Processor to memory: The processor writes a unit of data to memory.

## Slide 14
• I/O to processor: The processor reads data from an I/O device via an I/O module. • Processor to I/O: The processor sends data to the I/O device. • I/O to or from memory: For these two cases, an I/O module is allowed to exchange data directly with memory, without going through the processor, using direct memory access (DMA).

## Slide 16
2. Input/output Organization

## Slide 17: Input /Output Organization
The input output organization of computer depends upon the size of computer and the peripherals connected to it. The i/o subsystem of computer provides an efficient mode of communication between the central system and the outside environment.

## Slide 18: I/O Interface
The method of transfer of information between internal storage and external I/O devices is known as I/O interface.
The CPU is interfaced using special communication links by the peripherals connected to any computer system.
These communication links are used to resolve the differences between CPU and peripheral.
Interface units: There exists special hardware components between CPU and peripherals to supervise and synchronize all the input and output transfers.

## Slide 19
Mode of Transfer
The binary information that is received from an external device is stored in the memory unit.
The information that is transferred from the CPU to the external device is originated from the memory unit.
CPU merely processes the information but the source and target is always the memory unit.
Data transfer between CPU and the I/O devices may be done in different modes.
Data transfer to and from the peripherals may be done in three possible ways:-
Programmed I/O.
Interrupt- initiated I/O.
Direct memory access( DMA).

## Slide 20
Interrupt Driven I/O
By using interrupt facility to inform the interface to issue an interrupt request signal whenever data is available from any device.
In the meantime the CPU can proceed for any other program execution.
The interface meanwhile keeps monitoring the device.
Whenever it is determined that the device is ready for data transfer it initiates an interrupt request signal to the computer.

## Slide 21: Priority Interrupt I/O
Priority Interrupt System
The concept of defining the priority among devices so as to know which one is to be serviced first in case of simultaneous requests .
This involves two types:
Software method
ex - Polling
Hardware method
ex – Daisy chaining

## Slide 22: Direct Memory Access
The data transfer between a fast storage media such as magnetic disk and memory unit is limited by the speed of the CPU
we can allow the peripherals directly communicate with each other using the memory buses, removing the intervention of the CPU.

## Slide 23
During DMA the CPU is idle and it has no control over the memory buses.
The DMA controller takes over the buses to manage the transfer directly between the I/O devices and the memory unit.

## Slide 24
Bus Request :
It is used by the DMA controller to request the CPU to relinquish the control of the buses.
Bus Grant :
It is activated by the CPU to Inform the external DMA controller that the buses are in high impedance state and the requesting DMA can take control of the buses.
Once the DMA has taken the control of the buses it transfers the data. This transfer can take place in many ways.
Types of DMA transfer using DMA controller:
Burst transfer
Cyclic stealing
Interleaved mode

## Slide 25: I/O Processor
The Input Output Processor (IOP) is just like a CPU that handles the details of I/O operations.
The IOP can fetch and execute its own instructions.
In addition to the I/O – related tasks, it can perform other processing tasks like arithmetic, logic, branching and code translation.
The main memory unit takes the pivotal role.
It communicates with processor by the means of DMA.

## Slide 26
ADVANTAGES:
The I/O devices can directly access the main memory without the intervention by the processor in I/O processor based systems.
It is used to address the problems that are arises in Direct memory access method.

## Slide 27: Synchronous Data Transfer
In Synchronous data transfer, the sending and receiving units are enabled with same clock signal.
The master performs a sequence of instructions for data transfer in a predefined order.
All these actions are synchronized with the common clock.
Both the master and slave performs their own task of transferring data at designed clock period.

## Slide 28: Asynchronous Data Transfer
Asynchronous input output is a form of input output processing that allows others devices to do processing before the transmission or data transfer is done.
This problem is solved by following mechanism:
Strobe
Handshaking

## Slide 29: Strobe mechanism
Source initiated Strobe –
When source initiates the process of data transfer. Strobe is just a signal.
(i) First, source puts data on the data bus and ON the strobe signal. (ii) Destination on seeing the ON signal of strobe, read data from the data bus. (iii) After reading data from the data bus by destination, strobe gets OFF.
Destination initiated signal –
When destination initiates the process of data transfer.
(i) First, the destination ON the strobe signal to ensure the source to put the fresh data on the data bus. (ii) Source on seeing the ON signal puts fresh data on the data bus. (iii) Destination reads the data from the data bus and strobe gets OFF signal.

## Slide 30: Peripheral Devices
It is any auxiliary device that connects to and works with the computer to either put information into it or get information out of it.
A peripheral device may also be referred to as an external peripheral, integrated peripheral, auxiliary component, or I/O (input/output) device.
They are basically of three types:
Input Devices
Output Devices
Storage Devices

## Slide 31: Keyboard
Inside the keyboard, there are metallic plate, circuit board and processor, which are responsible for transferring information from the keyboard to the computer. Depending upon the working principle, there are two main types of keys, namely, capacitive and hard-contact. Let's discuss in brief about the functioning of capacitive and hard contact key.When a capacitive key is pressed, the metal plunger applies a gentle pressure to the circuit board. The pressure is identified by the computer and the circuit flow is initiated, resulting in the transfer of information from the circuit to the currently installed software. The key identifying to computer is identified using a keyboard driver and finding the preferred key called source code.

## Slide 32: Scanner
A scanner is a device that is used for producing an exact digital image replica of a photo, text written in paper, or even an object. This digital image can be saved as a file to your computer and can be used to alter/enhance the image or apply it to the web. The most commonly used scanner is the flatbed scanner, in which you keep the object on top of the glass window. The scanned output will be obtained in your computer. The image and text are obtained exactly through the process of optical character recognition .

## Slide 33
Handheld scanners use the same basic technology as a flatbed scanner, but rely on the user to move them instead of a motorized belt. This type of scanner typically does not provide good image quality. However, it can be useful for quickly capturing text. The basic principle of a scanner is to analyze an image and process it in some way. Image and text capture (optical character recognition or OCR) allow you to save information to a file on your computer.

## Slide 34
Drum scanners are used by the publishing industry to capture incredibly detailed images. They use a technology called a photomultiplier tube (PMT). In PMT, the document to be scanned is mounted on a glass cylinder. At the center of the cylinder is a sensor that splits light bounced from the document into three beams. Each beam is sent through a color filter into a photomultiplier tube where the light is changed into an electrical signal.
The basic principle of a scanner is to analyze an image and process it in some way. Image and text capture (optical character recognition or OCR) allow you to save information to a file on your computer.

## Slide 35: Mouse
A mouse is play a important role play in computers all the work. A mouse has a small size but its works is very large.
Working of a mouse: With most of the system you will find mechanical mouse. The primary mechanical part of a mouse is a ball on the bottom of the mouse. There are these little wheels which turn/rotate when the ball moves against them. The wheels are monitored electronically. When they turn or rotate they transmit how much they have turned to the computer. Out of these three wheels the two wheels perpendicular to each other are used for tracking the motion on X-axis and Y-axis. The third one just balances the two.

## Slide 36: Mouse
When the mouse is moved on a flat surface the roller ball moves in the locking ring. When the mouse is positioned on the desktop the actuators register the mouse balls movement in X-axis and Y-axis direction. The sensors attached to it generate a series of pulses representing movement on both axis. The pulse generated are in same ratio as the mouse movement i.e. More pulse mean more movement. Normally a mouse is used along with a mouse pad. Place the mouse pad on a flat surface and place the mouse on it. Move the mouse pad and the pointer moves in the direction of the movement of mouse.

## Slide 37: Video Display
Video display device means an electronic device with an output surface that displays, or is capable of displaying, moving graphical images or a visual representation of image sequences or pictures, showing a number of quickly changing images on a screen in fast succession to create the illusion of motion, including, if applicable, a device that is an integral part of the display, in that it cannot be easily removed from the display by the consumer, that produces the moving image on the screen. A video display device may use, but is not limited to, a cathode ray tube (CRT), liquid crystal display (LCD), gas plasma, digital light processing, or other image projection technology.

## Slide 38: Touch Screen
Different kinds of touchscreen work in different ways. Some can sense only one finger at a time and get extremely confused if you try to press in two places at once. Others can easily detect and distinguish more than one key press at once. There are various technologies.

## Slide 39: Infrared Technology of Touch Screen
Just like the magic eye beams in an intruder alarm, an infrared touchscreen uses a grid pattern of LEDs and light-detector photocells arranged on opposite sides of the screen. The LEDs shine infrared light in front of the screen—a bit like an invisible spider's web. If you touch the screen at a certain point, you interrupt two or more beams. A microchip inside the screen can calculate where you touched by seeing which beams you interrupted. The touchscreen on Sony Reader eBooks (like the one pictured in our top photo) works this way. Since you're interrupting a beam, infrared screens work just as well whether you use your finger or a stylus

## Slide 40
3.Memory Organization

## Slide 41: Memory organisation
Memories are made up of registers. Each register in the memory is one storage location. Storage location is also called as memory location. Memory locations are identified using Address. The total number of bit a memory can store is its capacity.
A storage element is called a Cell. Each register is made up of storage element in which one bit of data is stored. The data in a memory are stored and retrieved by the process called writing and reading respectively.
A word is a group of bits where a memory unit stores binary information. A word with group of 8 bits is called a byte.
Data lines provide the information to be stored in memory. The control inputs specify the direction transfer. The k-address lines specify the word chosen.

## Slide 42: Memory Hierarchy
In the Computer System Design, Memory Hierarchy is an enhancement to organize the memory such that it can minimize the access time. The Memory Hierarchy was developed based on a program behavior known as locality of references. The figure below clearly demonstrates the different levels of memory hierarchy.

## Slide 43: There are basically two division : Primary and auxiliary Memory as shown below.

## Slide 44
We can infer the following characteristics of Memory Hierarchy Design:
Capacity: It is the global volume of information the memory can store. As we move from top to bottom in the Hierarchy, the capacity increases.
Access Time: It is the time interval between the read/write request and the availability of the data. As we move from top to bottom in the Hierarchy, the access time increases.

## Slide 45
Performance: Earlier when the computer system was designed without Memory Hierarchy design, the speed gap increases between the CPU registers and Main Memory due to large difference in access time. This results in lower performance of the system and thus, enhancement was required. This enhancement was made in the form of Memory Hierarchy Design because of which the performance of the system increases. One of the most significant ways to increase system performance is minimizing how far down the memory hierarchy one has to go to manipulate data.

## Slide 46
Cost per bit: As we move from bottom to top in the Hierarchy, the cost per bit increases i.e. Internal Memory is costlier than External Memory.
A memory unit is the collection of storage units or devices together. The memory unit stores the binary information in the form of bits. Generally, memory/storage is classified into 2 categories:
Volatile Memory: This loses its data, when power is switched off.
Non-Volatile Memory: This is a permanent storage and does not lose any data when power is switched off.

## Slide 47: Internal Memory
Internal memory typically refers to main memory (RAM), but may also refer to ROM and flash memory. In either case, internal memory generally refers to chips rather than disks or tapes.
In a computer, all of the storage spaces that are accessible by a processor without the use of the computer input-output Internal memory usually includes several types of storage, such as main storage, cache memory, and special registers, all of which can be directly accessed by the processor.
Primary storage (or main memory or internal memory), often referred to simply as memory, is the only one directly accessible to the CPU. The CPU continuously reads instructions stored there and executes them as required. Any data actively operated on is also stored there in uniform manner.

## Slide 48: Random Access Memory(RAM)
Random access memory, or RAM, is memory storage on a computer that holds data while the computer is running so that it can be accessed quickly by the processor. RAM holds the operating system, application programs and data that is currently being used.
RAM data is much faster to read than data stored on the hard disk. RAM is stored in microchips and contains much less data than the hard disk.

## Slide 49
RAM can never run out of memory, but the processor must overwrite old data if the RAM is filled, which results in slower computer function. Any file stored in RAM can be accessed directly if the user knows the row and column where the data is stored. Random access memory is used to store temporary but necessary information on a computer for quick access by open programs or applications.
RAM, is a volatile yet fast type of memory used in computers. RAM is more expensive to incorporate.
RAM allows reading and writing (electrically) of data at the byte level
RAM is the Volatile memory.

## Slide 50: Static RAM
Is a type of RAM.
Static RAM stores a bit of information in a flip-flop. Static RAM is usually used for applications that do not require large capacity RAM memory.
Static(RAM) is a memory technology based on flip-flops. SRAM has an access time of 2 – 10 nanoseconds. All of main memory can be viewed as fabricated from SRAM, although such a memory would be unrealistically expensive

## Slide 51: Dynamic RAM
Dynamic RAM data store one bit of information as a payload. Dynamic RAM using a substrate capacitance gate MOS transistors as memory cells shut. To keep dynamic RAM stored data remains intact, the data should be refreshed again by reading and re-write the data into memory. Dynamic RAM is used for applications that require large RAM capacity, for example in a personal computer. EDO (Extended Data-output) and SD (Synchronous Dynamic Random Access Memory) are type of Dynamic RAM.

## Slide 52
Dynamic RAM (DRAM) is a memory technology based on capacitors. Dynamic RAM is cheaper than static RAM and can be packed more densely on a computer chip
DRAM has an access time in the order of 60 – 100 nanoseconds, slower than SRAM.

## Slide 53: Read Only Memory(ROM)
Sometimes can be erased for reprogramming, but might have odd requirements such as UV light or erasure only at the block level.
Data are written into a ROM when it is manufactured.
ROM is mask programmed by the manufacturer in the factory with the contents ordered by the customers.
The contents are fixed by metal masks used during chip fabrication.
Once programmed, the contents cannot be erased.
Even a single bit wrongly programmed the ROM chip is useless

## Slide 54: Types of ROM
PROM (Programmable Read Only Memory)
EPROM (Erasable Programmable Read Only Memory )
EEPROM (Electrically Erasable Programmable Read Only Memory)

## Slide 55: PROM (Programmable Read Only Memory)
PROM is a field programmable device.
The customer buy a blank PROM and store desired data using PROM programmer(burner).
Programmability achieved by inserting a fuse at point P.
Before programmed, the memory contains all 0s
The user can insert 1 by burning out the fuse in the particular cell using high current pulse.

## Slide 56
The PROM chip can be programmed only once and its contents cannot be erased.
PROM are flexible, faster and less expensive because they can be programmed directly by the user.

## Slide 57: EPROM
A rewritable chip that holds its contents without power. Previous data can be erased and new data can be inserted
EPROM chips are written on an external programming device before being placed on the circuit board. Capable of retaining stored information for a long time.
Eraser contd., requires breakup the charges trapped in the transistors of memory cell.[this is done by break the chip to ultraviolet light].
This reason EPROM packaged with transparent window.

## Slide 58
Drawback: Entire EPROM is erased as a whole and selective erasing is not possible. Should be removed from the chip for reprogramming.
Unlike the PROM, EPROM contents can be deleted after being programmed. Elimination is done by using ultraviolet light.

## Slide 59: EEPROM (Electrically Erasable Programmable Read Only Memory)
EEPROM can store data permanently, but its contents can still be erased electrically through the program. One type EEPROM is Flash Memory. Flash Memory commonly used in digital cameras, video game consoles, and the BIOS chip.
It can be both programmed and erased electrically ( flashed back to Zero).
They do not need to removed when the chip content erasure.
Also, erase selected content in the chip.
Erasing and programming dynamically without removing the EEPROM from the circuit

## Slide 60: External Memory
External memory typically refers to storage in an external hard drive or on the Internet. The main “memory” in the computer is the computer work-space, not its storage facility.
External memory which is sometimes called backing store or secondary memory, allows the permanent storage of large quantities of data. Some method of magnetic recording on magnetic disks or tapes is most commonly used.
The capacity of external memory is high, usually measured in hundreds of megabytes or even in gigabytes
The most common form of external memory is a hard disc which is permanently installed in the computer and will typically have a capacity of hundreds of megabytes

## Slide 61: Cache Memory
Cache memory, also called CPU memory, is high-speed static random access memory (SRAM) that a computer microprocessor can access more quickly than it can access regular random access memory (RAM). This memory is typically integrated directly into the CPU chip or placed on a separate chip that has separate bus interconnect with the CPU. The purpose of cache memory is to store program instructions and data that are used repeatedly in the operation of programs or information that the CPU is likely to need next. The computer processor can access this information quickly from the cache rather than having to get it from computer’s main memory. Fast access to these instructions increases the overall speed of the program

## Slide 62
As the microprocessor processes data, it looks first in the cache memory. If it finds the instructions or data it's looking for there from a previous reading of data, it does not have to perform a more time-consuming reading of data from larger main memory or other data storage devices. Cache memory is responsible for speeding up computer operations and processing.
Once they have been opened and operated for a time, most programs use few of a computer's resources. That's because frequently re-referenced instructions tend to be cached. This is why system performance measurements for computers with slower processors but larger caches can be faster than those for computers with faster processors but less cache space.

## Slide 63: Cache Memory Mapping
Caching configurations continue to evolve, but cache memory traditionally works under three different configurations:
Direct mapped cache has each block mapped to exactly one cache memory location. Conceptually, direct mapped cache is like rows in a table with three columns: the data block or cache line that contains the actual data fetched and stored, a tag with all or part of the address of the data that was fetched, and a flag bit that shows the presence in the row entry of a valid bit of data.

## Slide 64
Fully associative cache mapping is similar to direct mapping in structure but allows a block to be mapped to any cache location rather than to a prespecified cache memory location as is the case with direct mapping.
Set associative cache mapping can be viewed as a compromise between direct mapping and fully associative mapping in which each block is mapped to a subset of cache locations. It is sometimes called N-way set associative mapping, which provides for a location in main memory to be cached to any of "N" locations in the L1 cache.

## Slide 65: Virtual Memory
Virtual memory is a memory management capability of an operating system (OS) that uses hardware and software to allow a computer to compensate for physical memory shortages by temporarily transferring data from random access memory (RAM) to disk storage.
Virtual address space is increased using active memory in RAM and inactive memory in hard disk drives (HDDs) to form contiguous addresses that hold both the application and its data.

## Slide 66
Virtual memory was developed at a time when physical memory -- the installed RAM -- was expensive. Computers have a finite amount of RAM, so memory can run out, especially when multiple programs run at the same time. A system using virtual memory uses a section of the hard drive to emulate RAM. With virtual memory, a system can load larger programs or multiple programs running at the same time, allowing each one to operate as if it has infinite memory and without having to purchase more RAM.
While copying virtual memory into physical memory, the OS divides memory into page files or swap files with a fixed number of addresses. Each page is stored on a disk and when the page is
needed, the OS copies it from the disk to main memory and translates the virtual addresses into real addresses.

## Slide 67
Among the primary benefits of virtual memory is its ability to handle twice as many addresses as main memory. It uses software to consume more memory by using the HDD as temporary storage while MMUs translate virtual memory addresses to physical addresses via the CPU. Programs use virtual addresses to store instructions and data; when a program is executed, the virtual addresses are converted into actual memory addresses.

## Slide 68: Secondary Memory
Secondary memory (or secondary storage) is the slowest and cheapest form of memory. It cannot be processed directly by the CPU. It must first be copied into primary storage (also known as RAM).
It is non-volatile, i.e. It retains data when power is switched off It is large capacities to the tune of terabytes
It is cheaper as compared to primary memory

## Slide 70: Magnetic Disk
A magnetic disk primarily consists of a rotating magnetic surface and a mechanical arm that moves over it. The mechanical arm is used to read from and write to the disk. The data on a magnetic disk is read and written using a magnetization process. Data is organized on the disk in the form of tracks and sectors, where tracks are the circular divisions of the disk. Tracks are further divided into sectors that contain blocks of data. All read and write operations on the magnetic disk are performed on the sectors.
Magnetic disks have traditionally been used as primary storage in computers. With the advent of solid-state drives (SSDs), magnetic disks are no longer considered the only option, but are still commonly used.

## Slide 71: CD Drive
CD stands for Compact Disk. CDs are circular disks that use optical rays, usually lasers, to read and write data. They are very cheap as you can get 700 MB of storage space for less than a dollar. CDs are inserted in CD drives built into CPU cabinet. They are portable as you can eject the drive, remove the CD and carry it with you. There are three types of CDs −
CD-ROM (Compact Disk – Read Only Memory) − The data on these CDs are recorded by the manufacturer. Proprietary Software, audio or video are released on CD-ROMs.

## Slide 72
CD-R (Compact Disk – Recordable) − Data can be written by the user once on the CD-R. It cannot be deleted or modified later.
CD-RW (Compact Disk – Rewritable) − Data can be written and deleted on these optical disks again and again.

## Slide 73: Magnetic Tape
Originally, magnetic tape was designed to record sound. In computing, it holds binary data. In recent years, magnetic tape devices have become more scarce with the emergence of digital imaging and audiovisual media storage.
Magnetic tape was used in many of the larger and less complex mainframe computers that predated today’s personal computers (PC).

## Slide 74
4. CPU Organization

## Slide 75: CPU
The part of computer that performs the bulk of data-processing operations is called central processing unit and is referred to as the CPU. The CPU is made up of three major parts.
The register set stores intermediate data used during the execution of the instructions.
The arithmetic logic unit(ALU) performs the required micro operations for executing the instructions.
The control unit supervises the transfer of information among the registers and instruct the ALU as to which operation to perform.

## Slide 76: General Register Organisation
When a large number of registers are included in the CPU, it is most efficient to connect them through a common bus system. The registers communicate with each other not only for direct data transfers, but also while performing various microoperations. Hence it is necessary to provide a common unit that can perform all the arithmetic, logic, and shift microoperations in the processor.
BUS SYSTEM
A bus organisation for seven CPU registers is shown. The output of each register is connected to two multiplexers(MUX) to form the two buses A and B. The selection lines in each mutliplexer select one register or the input data for the particular bus.

## Slide 78
The A and B buses from the inputs to a common arithmetic logical unit(ALU). The operation selected in the ALU determines the arithmetic or logic microoperation that is to be performed. The result of the microoperation is available for output data and also goes into the inputs of all the resisters. The resister that receives the information from the output bus is selected by a decoder. The decoder activates one of the register load inputs of the selected destination register.

## Slide 79: Control Word
There are 14 binary selection inputs in the unit, and their combined value specifies a control word . The 14-bit control word is defined in the fig. b. It consists of four fields. Three fields contain three bit each , and one has five bits. The three bit of SELA select a source register for the A input of the ALU. the three bits of SELD select a destination register for the B input of the ALU. The three bits of SELD select a destination register using the decoder and its seven load outputs. The five bits of OPR select one of the operations in the ALU. The 14- bit control word when applied to the selection inputs specify a particular microoperation.

## Slide 80: ALU
The ALU provides arithmetic and logic operations. In addition, the CPU must provide shift operations. The shifter may be placed in the input of the ALU to provide a preshift capability, or at the output of the ALU to provide post shifting capability. In some cases, the shift operations are included with the ALU. An arithmetic logic and shift unit was designed in Sec. 4-7. The function table for this ALU is listed in Table 4-8. The encoding of the ALU operations for the CPU is taken from Sec.4-7 and is specified in Table 8-2. The OPR field has five bits and each operation is designated with a symbolic name.

## Slide 81: Stack Organization
A useful feature that is included in the CPU of most computers is a stack or last-in, first-out (LIFO) list. A stack is a storage device that stores information in such a manner that the item stored last is the first item retrieved. The operation of a stack can be compared to a stack of trays. The last tray placed on top of the stack is the first to be taken off.
The stack in digital computers is essentially a memory unit with an address register that can count only ( after an inital value is loaded into it ). The register that holds the address for the stack is called a stack pointer (SP ) because its value always points at the top item in the stack. Contrary to a stack of trays where the tray itself may be taken out or inserted, the physical registers of a stack are always available for reading or writing. It is the content of the word that is inserted or deleted.

## Slide 82
The two operations of a stack are the insertion and deletion of items. The operation of insertion is called push ( or push-down ) because it can be thought of as the result of pushing a new item on top. The operation of deletion is called pop ( or pop-up ) because it can be thought of as the result of removing one item so that the stack pops up. However, nothing is pushed or popped in a computer stack.' The operations are simulated by incrementing or decrementing the stack pointer register

## Slide 83: Accumulator
The computers, present in the early days of computer history, had accumulator based CPUs. In this type of CPU organization, the accumulator register is used implicitly for processing all instructions of a program and store the results into the accumulator. The instruction format that is used by this CPU Organisation is One address field. Due to this the CPU is known as One Address Machine.
The main points about Single Accumulator based CPU Organisation are:
In this CPU Organization, the first ALU operand is always stored into the Accumulator and the second operand is present either in Registers or in the Memory.
Accumulator is the default address thus after data manipulation the results are stored into the accumulator.
One address instruction is used in this type of organization.

## Slide 84: One Address Accumulator
One Address Instructions – This use a implied ACCUMULATOR register for data manipulation. One operand is in accumulator and other is in register or memory location. Implied means that the CPU already know that one operand is in accumulator so there is no need to specify it.

## Slide 86: Two Address Instruction
This is common in commercial computers.Here two address can be specified in the instruction.Unlike earlier in one address instruction the result was stored in accumulator here result cab be stored at different location rather than just accumulator, but require more number of bit to represent address.

## Slide 88: Three Address Instruction
This has three address field to specify a register or a memory location. Program created are much short in size but number of bits per instruction increase. These instructions make creation of program much easier but it does not mean that program will run much faster because now instruction only contain more information but each micro operation (changing content of register, loading address in address bus etc.) will be performed in one cycle only.

## Slide 89
3. Control Unit

## Slide 90: Introduction to Word Format
Computer perform task on the basis of instruction provided.
A instruction in computer comprises of groups called fields.
These field contains different information as for computers every thing is in 0 and 1
The most common fields are:
Operation field which specifies the operation to be performed like addition.
Address field which contain the location of operand, i.e., register or memory location.
Mode field which specifies how operand is to be founded.
A instruction is of various length depending upon the number of addresses it contain. Generally CPU organization are of three types on the basis of number of address fields:
Single Accumulator organization
General register organization
Stack organization

## Slide 91: Fetch Cycle
Step 1: The address in the program counter is moved to the memory address register(MAR), as this is the only register which is connected to address lines of the system bus.

## Slide 92
Step 2: The address in MAR is placed on the address bus, now the control unit issues a READ command on the control bus, and the result appears on the data bus and is then copied into the memory buffer register(MBR). Program counter is incremented by one, to get ready for the next instruction.(These two action can be performed simultaneously to save time)

## Slide 93
Step 3: The content of the MBR is moved to the instruction register(IR

## Slide 94: Execute Cycle
Step 1: The address portion of IR is loaded into the MAR.
Step 2: The address field of the IR is updated from the MBR, so the reference memory location is read.
Step 3: Now, the contents of R and MBR are added by the ALU.

## Slide 95: Control of Arithmetic Operations
The ALU is a digital circuit that provides arithmetic and logic operation. It is the fundamental building block of central processing unit of a computer.

## Slide 96: BUS
In early computers “BUS” were parallel electrical wires with multiple hardware connections.
Therefore a bus is communication system that transfers data between component inside a computer, or between computers. It includes hardware components like wires, optical fibers, etc and software, including communication protocols.
The Registers, ALU and the interconnecting BUS are collectively referred as data path.
Types of bus are:
Address bus: The buses which are used to carry address.
Data bus: The buses which are used to carry data.
Control bus: If the bus is carrying control signals .
Power bus: If it is carrying clock pulse, power signals it is known as power bus, and so on.

## Slide 97: BUS
Program Counter – A program counter (PC) is a CPU register in the computer processor which has the address of the next instruction to be executed from memory. As each instruction gets fetched, the program counter increases its stored value by 1. It is a digital counter needed for faster execution of tasks as well as for tracking the current execution point.
Instruction Register – In computing, an instruction register (IR) is the part of a CPU’s control unit that holds the instruction currently being executed or decoded. An instruction register is the part of a CPU’s control unit that holds the instruction currently being executed or decoded. Instruction register specifically holds the instruction and provides it to instruction decoder circuit

## Slide 98: BUS
Memory Address Register – The Memory Address Register (MAR) is the CPU register that either stores the memory address from which data will be fetched from the CPU, or the address to which data will be sent and stored. It is a temporary storage component in the CPU(central processing unit) which temporarily stores the address (location) of the data sent by the memory unit until the instruction for the particular data is executed.
Memory Data Register – The memory data register (MDR) is the register in a computer’s processor, or central processing unit, CPU, that stores the data being transferred to and from the immediate access storage. Mmemory data register (MDR) is also known as memory buffer register (MBR).
General Purpose Register – General purpose registers are used to store temporary data within the microprocessor. It is a multipurpose register. They can be used either by programmer or by a user.

## Slide 99: Micro Programming Concepts
The control signals associated with operations are stored in special memory units inaccessible by the programmer as Control Words.
Control signals are generated by a program are similar to machine language programs.
Micro-programmed control unit is slower in speed because of the time it takes to fetch microinstructions from the control memory.

## Slide 100
Some Important Terms –
Control Word : A control word is a word whose individual bits represent various control signals.
Micro-routine : A sequence of control words corresponding to the control sequence of a machine instruction constitutes the micro-routine for that instruction.
Micro-instruction : Individual control words in this micro-routine are referred to as microinstructions.
Micro-program : A sequence of micro-instructions is called a micro-program, which is stored in a ROM or RAM called a Control Memory (CM).
Control Store : the micro-routines for all instructions in the instruction set of a computer are stored in a special memory called the Control Store.